## Slide 1: VC106 Vapor Control Systems John Zink Company Background
Reforming Furnaces

## Slide 2: Top-Fired Reformer
Consists of a firebox containing anywhere from 1 to several rows of tubes
Process gas flows downward through the catalyst filled tubes
Burners are located in between the tube rows in the top of the firebox & are located at one level (above grade)
Tubes are heated by radiation from the flames, flue gas and some convective effects
Process gas and flue gas flow is co-current with both exiting at the bottom of the firebox (allows for rapid heating of the hydrocarbon steam mixture)
Additional heat recovery takes place in the convection section which is typically located at grade
This type of furnace arrangement can accommodate small to very large capacities within a single firebox

## Slide 3: Top-Fired Reformer
Catalyst-filled process tube (typical)
Downfired burner (typical)
Flue gas exhaust
Process flow
Notes: Consists of a firebox containing anywhere from 1 to several rows of tubes.
Process gas flows downward through the catalyst filled tubes.
Burners are located in between the tube rows in the top of the firebox & are located at one level (above grade).
Tubes are heated by radiation from the flames, flue gas and some convective effects.
Process gas and flue gas flow is co-current with both exiting at the bottom of the firebox (allows for rapid heating of the hydrocarbon steam mixture).
Additional heat recovery takes place in the convection section which is typically located at grade.
This type of furnace arrangement can accommodate small to very large capacities within a single firebox.

## Slide 4: Side-Fired Reformer
Side fired reformer consists of catalyst tubes positioned in a single row along the centerline of the firebox
Due to the layout, this type of furnace arrangement results in a long narrow firebox
Burners are located at multiple levels on the two sidewalls of the firebox and evenly distributed over the entire wall
Tubes are heated by radiation from the walls, flue gas and, to a small extent, convective effects
Process gas flow through the catalyst tubes is downward while the flue gas flow is upward
For large capacities, it is common to have multiple fireboxes located side by side sharing a common inlet distribution and outlet collection system & waste heat recovery section

## Slide 5: Side-Fired Reformer
Catalyst-filled process tube (typical)
Side-fired burner (typical)
Flue gas exhaust
Process flow
Notes: Side fired reformer consists of catalyst tubes positioned in a single row along the centerline of the firebox.
Due to the layout, this type of furnace arrangement results in a long narrow firebox.
Burners are located at multiple levels on the two sidewalls of the firebox and evenly distributed over the entire wall.
Tubes are heated by radiation from the walls, flue gas and, to a small extent, convective effects.
Process gas flow through the catalyst tubes is downward while the flue gas flow is upward.
For large capacities, it is common to have multiple fireboxes located side by side sharing a common inlet distribution and outlet collection system & waste heat recovery section.

## Slide 6: Terrace-Wall Fired Reformer
A refinement of the sidewall fired reformer in that many of the salient features previously described are similar, but with 2 major differences:
  number of burners
  type of burners
Typically uses 2 levels of firing & therefore results in fewer burners for a given capacity
Primary objective is to allow a controlled temperature profile along the length of the tube

## Slide 7: Terrace-Wall Fired Reformer
Catalyst-filled process tube (typical)
Upfired burner (typical)
Flue gas exhaust
Process flow
Notes: A refinement of the sidewall fired reformer in that many of the salient features previously described are similar, but with 2 major differences:
  number of burners
  type of burners
Typically uses 2 levels of firing & therefore results in fewer burners for a given capacity.
Primary objective is to allow a controlled temperature profile along the length of the tube.